## Slide 1: Open Pyrojet – RocketPrinter
FDM printer modified to print metal, ceramic and high temperature plastics, without compromising resolution and speed.

## Slide 2: Basic System Layout
Air Induction
(Air Pump)
Material Feed Venturi
Material Suspension Tank
(0.5-30 micron powder in Ethanol/other fuel)
FDM Printer Bowden Tube to standard hot-end
Valve

## Slide 3: Basic System Layout
Air Induction
Peristaltic Pump
Material Feed Venturi
FDM Printer Bowden Tube to standard hot-end
Material Feel Peristaltic Pump

## Slide 4: Basic System Layout
FDM Printer Bowden Tube to standard hot-end
Heat sink
Heat Break
Heat Block
Flame spray
Build Plate
Air+Fuel+Material Flow
Combustion of Air+Fuel
Material Melts

## Slide 5: Basic System Description-
Air is pulled from atmosphere and forced through a venturi which generates a vacuum that entrains and atomizes fuel and suspended materials from a tank.
This air/fuel/material mixture is fed through the Bowden system of a standard FDM printer such as an ender3 or prusa mini, ultimately to arrive at the hotend for ignition.
The hotend heater and block achieve the autoignition temperature of the air/fuel/material mixture and start it combusting through the extruder nozzle.
The combustion process accelerates the mixture out the nozzle, melts the entrained material particles and consumes the oxygen in the nozzle and air gap between nozzle and build plate.
The now molten particles surrounded by combustion byproducts deposit on the build plate and form a part, layer by layer, in the same fashion as FDM.

## Slide 6: Basic System Description_PeristalticPumps-
Air is pulled from atmosphere and forced through a venturi and mixing chmber where fuel is injected via a similar peristaltic pump drawing from a suspension of particles in fuel. This air/fuel/material mixture is fed through the Bowden system of a standard FDM printer such as an ender3 or prusa mini, ultimately to arrive at the hotend for ignition.
The hotend heater and block achieve the autoignition temperature of the air/fuel/material mixture and start it combusting through the extruder nozzle.
The combustion process accelerates the mixture out the nozzle, melts the entrained material particles and consumes the oxygen in the nozzle and air gap between nozzle and build plate.
The now molten particles surrounded by combustion byproducts deposit on the build plate and form a part, layer by layer, in the same fashion as FDM.